cangateBMS is primary a tool for development and debugging of the BMS.

CangateBMS commands for polling and responses

The purpose of the ‘e’ command is to send poll CAN msgs to the BMS board and simulate what the EMC will be doing. Since the poll msg can elicit a response from a single BMS node, a string, or all, responses for specific CAN ID are displayed with a separate command, ‘a’ and multiple instances of the ‘a’ command would be needed if a poll from a cangateBMS instance using the ‘e’ command results in multiple BMS nodes responding.

Command ‘e’ is intended to poll BMS nodes and command ‘a’ is intended to display BMS responses. The polling can be to a specific BMS node, a string, or all BMS nodes. The display is to a specific BMS CAN id.

A single poll msg could cause six nodes on a string to respond, each sending six CAN msgs with cell readings, but a single instance of cangateBMS running the ‘a’ command would only display the cell readings for one specific BMS node.

Some CAN msg commands can turn on|off the HEATER, DUMP, DUMP2, and discharge FETs. However, the BMS software attempts to prevent any cell from being over charged, or under discharged so the CAN command might be overridden depending on the situation.

DUMP2 is assumed to control an external module charger and it is turned off when the first cell reaches the max target voltage and it is in charging mode (hyster_sw = 0). With the mode as a bit in the status msg, the EMC local node can use that to turn off string charging. When the BMS is in the charge mode and no cells have reached max, DUMP2 is turned on. When all the cells have tripped the max level the mode switches to self-discharge mode (hyster_sw = 1). A CAN msg command cannot turn DUMP2 on. However, a CAN msg can set the mode back to charge, i.e. hyster_sw = 0. The BMS program will turn DUMP2 on, but a CAN msg can also turn it off (and back on), until the first cell trips the max voltage limit.

command e – Send CAN msgs to BMS (polling)

ew – Sets the BMS CAN ID when sending a poll msg to a specific BMS board.
Initial default is B0A00000
ew 0 sets it to “all”, but not necessary to to do this.
ew xxxxxxxx sets the CAN ID that is saved in common so until the program is reloaded this CAN ID will be used for polling a specific BMS.

For polling a specific BMS node, the commands have ‘m’ for the second char--
emx
   x = j get a reading
   x = k send a setting

For polling all BMS nodes, the commands have ‘a’ for the second char--
eax
   x = j get a reading
   x = k send a setting

ed – Sets the duration (ms) between sending poll msgs.
Initial default is 1000 (1.000 secs)
ed 0 – sends just one msg.
ed 2000 – would send a msg every 2.000 seconds.
The setting is saved in common so until the program is reloaded the last saved setting remains in effect.

er – Sets the ADC rate in the ADBMS1818.
Default code = 0: 422 Hz)
er 8 (greater) displays list of codes versus ADC rates and ADC conversion delay (usec) (code = 4 is “normal” 7 Khz)
er <0-7> uses rate from table.
The adc rate is saved in common.

ep – Sets msg this program sends to poll, i.e. the “poller”.
Default: B0200000 (generally used by the PC)
B0000000 is reserved for the EMC

Any CAN ID can be used, but the BMS nodes must have the CAN ID in their parameter file, and only two are currently specified. This might need to be expanded to include EMC/MMC local and EMC/MMC master IDs.

x = a (e.g. ema (specific BMS) or eaa (all BMS) ) Polls cell readings)
Eighteen cell readings are returned in six CAN msgs for each poll msg sent.
Polling rate is set by the ed (or default)
ADC conversion rate set by the er (or default)
Poller and BMS CAN ids set by ep and er (or default)